## Slide 1: Implementation of control systems and future trends at the Martin-Luther-University using 4DIAC
Scientific work of Dipl.-Ing. Christian Gerber

## Slide 2: Implementation of Distributed Control Systems
Using several testbeds
  Festo Manufacturing System
  EnAS-Demonstrator
  Simulation of a Servo-Control-System
Using different Engineering Environments and Hardware
  Function Block Development Kid (FBDK)
  Framework for Distributed Industrial Automation and Control (4DIAC)
  FBench
  Corfu ESS
  ISAGraph
Usability test of several control implementation approaches
  Central-Controller
  Master-Task-Controller
  Parametrised Master-Task-Controller
  Workpiece-Controller

## Slide 3: Energy autarkic Actuator Sensor System Demonstrator
testbed, equipped with a wireless actuator/sensor system (2007-09)  new SIFB
Base Station + Sensor-Actuator Modules
  2,4 GHz with frequency adaptation to the gaps of WLAN
  1st phase – initialisation, get all Sensor-Actuator Modules
  2nd phase – real time wireless communication – time sliced
Control and Base Station exchange messages as follow: 76 00 03 52 FF 00 FF 00 FF 00
  1. Byte - Identifier the following data is an array (76)
  2. & 3. Byte - Length of the array (data values)
  4. Byte - datatype of the contained values (52)
  5. & 6. Byte - Low and HighByte SAM0 (FF 00)
  7. & 8. Byte - Low and HighByte SAM1 (FF 00)
  9. & 10. Byte - Low and HighByte SAM2 (FF 00)

## Slide 4: Central-Controller Approach
Central-Controller of the left plant part
  No reconfiguration possibility or reusability (one monolithic FB)
  Load Workpiece into tin– green
  Unload Workpiece from tin – red
  Close a tin - blue
  Move conveyor - brown

## Slide 5: Parameterized Master-Task-Controller
Task-Controller of the Jack Station
  Reuseable, if the component is used again
  Load Workpiece into tin – green
  Unload Workpiece from tin – red

## Slide 6: Parameterized Master-Task-Controller
Function Block Network of the Master and Task-Controller controlling the Jack-Station
  Using Adapter Interfaces as Sockets

## Slide 7: Parameterized Master-Task-Controller
Master-Controller
  Reconfiguration by implementing all production possibilities and parameterize the production scenario
  Actions – Array (sequence) of actions to perform
  Length – amount of sequenced actions

## Slide 8: Parameterized Master-Task-Controller – Resource Mapping
Without Adapter Interfaces
  Reconfiguration is missing due to a better visualisation of the FBN
  Subapplication encapsulates the Master and Task-Controller
  SIFB to the right and left
  Everytime a FB is changed, update data connections
With Adapter Interfaces
  Each FB provides an adapter corresponding to the one of the I/O-Adapter FB (Process Interface)  only one Adapter Connection if a FB is changed

## Slide 9: Automatic Generation of the I/O-Adapter
Eclipse-PlugIn for 4DIAC
Apdapter inserted from the pallet as new group (grey headline)
  Inputs and Outputs
  Comment
  DataType
General
  Define used SIFB
  PubInputs
  PubOutputs
  Time to ReRead the inputs
Define Adress

## Slide 10: Automatic Generation of the I/O-Adapter
Generated I/O-Adapter
  Textual representation eases maintenance (data connection results from adress)
  Reconnection by providing a new adress
  Export to LaTex  PDF generation for documentation

## Slide 11: Developing a Production Scenario
SysML Activity Diagram
  Partition for each control of a mechanical component
  Pallet 1 – blue
  Pallet 2- red
  Pallet 3 – green
Note the actions to be performed
Array of Actions
  From top to down
  Translate to numbers according to the tables
Parameterize new productoin scenario via HMI
Complexity shifted from the development of the Master-Controller to the production scenario

## Slide 12: Future Work - Workpiece-Controller
Improvement of the Parameterized Master-Task Controller approach with an additional coordination layer  The Workpiece-Controller
Workpiece Controller allocates /deallocates Master controller
Master-Controller is a kind of event multiplexer (see ECC)
Additional Inputs
  Actions - [INT]  Action INT
  Assign – INT
Additional Outputs
  Available – BOOL
  AssignedTo – INT
Additional Algorithms
  Allocate Available := False; AssignedTo := Assign;
  Deallocate Available := True; AssignedTo := 0;

## Slide 13: Future Work – Workpiece-Controller
Digi-Connect-Wi-Me
  Workpiece-Controller at the pallet
  Energy supply ?
Beckhoff CX8000
  Jack, Slide and Gripper Station through the wireless auctuator sensor system
Wago IPC 750-860
  Jack and Slide Station
Auvis.pro
  All 3 left conveyors
Auvis.box
  1 conveyor each as well as the Gripper Station
WebServer at all of them
  Linked websites between all

## Slide 14: Future Work – Closed-Loop 3d Simulation
Export CAD – Data of non-moving and moving parts as 3D Models
  3ds files– AutoCAD, Autodesk
  VRML files – Solid Edge, Solid Works
Simulation Tool - Enterprise Dynamics
  Modelling of process flows (Sources, Servers, Sinks)
  Based on atoms and subatoms
    e.g. Pallet is a subatom of the conveyor
  Communication between atoms via channels (listen to events, exchange subatoms)
  2D and 3D models
  Extendable by external libraries e.g. communication via Profibus to a Siemens PLC  new library to communicate with a distributed control system
  e.g. TCP-Socket encoding and decoding messages according to the compliance profile

## Slide 15: Communication with a Siemens PLC
Create a DataFB (definition of a Struct to save data)
  Read and writing to the struct
  Data encoding
  Data decoding (Compliance profile of the IEC 61499)
Provide a Server Socket
Call “AG_Send” with startposition at the DataFB and the length
Call “AG_Recv” with startposition at the DataFB and the length

## Slide 16: Future Work – Instant Start-Up after Power Down
Extension of the management resource with the FB StartUp of the type DEV_StartUp
Initialized after the MGR FB
Checks if the File exists
  If true - while EOF
    read xml-element
    encode it to a destination and request
    wait for response
    Check response
publish INITO+  initialize the SVR
REQ_Server(DST, RQST)
  Store DST and RQST at the File
  CNF(DSTO, RQSTO)
Device still has the management interface as well as a Start-Up configuration up to the last change

## Slide 17: Formal Controller Modelling
Definition of several rules to transform
  simple and basic FBs
  Function networks and composite FBs as well as application
Modelling of Process and Communication Interface (SIFB)
  Service primitives (ISO-IEC 10731)
Modelling of resources
  Include the different schedulings of FBs (Scheduling Function)
Modelling of devices

## Slide 18: Formal Plant and Closed-Loop Modelling
Modelling of the mechanical components
Modelling of the workpiece behaviour
Establishing the Closed-Loop

## Slide 19: Verification of the Closed-Loop System
SWI-Prolog based TNCES-Workbench
  Model-Checker
  FB Transformator
  Search for trajectories and Gantt-Chart Visualisation …
Analysis of different FB schedules
Analysis of counter examples and modifying the control

## Slide 20: Thanks for your attention!
Christian Gerber
Chair of Automation Technology
30.08.2010
http://aut.informatik.uni-halle.de
Supported by:
  German Ministry for Commerce and Industry (BMWI)
  Deutsche Forschungsgemeinschaft (DFG)
  Festo AG & Co. KG)